## Slide 1: Unified Simulation Environment
21 May 2020
UNCLASSIFIED // NOT APPROVED FOR PUBLIC RELEASE
UNCLASSIFIED // NOT APPROVED FOR PUBLIC RELEASE
Notes: 1
1

## Slide 2: Architecture
Support unified simulation environments:
1. Behavioral mode (BFM/fast)
2. BARE Metal (RISC-V RTL/slow)
3. Linux (HW card/super fast)
4. Individual Unit level test benches. One per HW assist core. Supports 2 modes:
Clock Cycle accurate.
TileLink Transaction level accurate
C2 – Command and Control, KL- Key Load, LLC – Logic Locked Core, TSS – Technique Specific Shim
CEP with LLKI

## Slide 3: BFM Mode
Each RISC-V core is replaced with a behavioral model that only support TileLink transactions.
Test is running on native machine with hooks to control the BFM model to execute TL transactions (via Direct Programing Interface).
Test also support capture mode (TL transaction level or cycle-by-cycle) to a header file for playback in BARE Metal mode and unit level (e.i aes_playback.h)
C_module wrapper
RISC-V
BFM Model
titleLink Bus
C/C++ Test
<core>_playback.h
(transaction accurate)
If enable
<core>_stimulus.txt
(cycle accurate)

## Slide 4: BARE Metal Mode
RISC-V is actual RTL code
Test is wrapped inside RISC-V wrapper and cross compiled to ELF executable file to be loaded into DDR3 memory (via backdoor).
<core>_playback.h, captured from BFM mode, is executed by actual RISC-V transaction-by-transaction.
titleLink Bus
RISC-V wrapper
<core>_playback.h
playback.cc

## Slide 5: Linux Mode
. FPGA is synthesize, place/route to obtain mcs file and loaded onto VC707 eval card.
Linux OS is built with cep_diag application (which includes all simulation tests) as diagnostic
titleLink Bus
Linux OS
test1
cep_diag.cc
testN
. . .
VC707 Eval Card

## Slide 6: Playback File Format
Below is one example of the <core>_playback.h file format to be used in BARE Metal or Unit-Level testbench.
// Write to : <physicalAdr> <writeData>
#define WRITE__CMD 1
// Read and compare: <physicalAdr> <Data2Compare>
#define RDnCMP_CMD 2
// Read and spin until match : <physicalAdr> <Data2Match> <mask> <timeout>
#define RDSPIN_CMD 3
// dft command sequences to playback
uint64_t dft_playback[] = {
WRITE__CMD, 0x70050010, 0x0001000000000000 // 1
, WRITE__CMD, 0x70050008, 0x0000000000000000 // 2
<...>
, WRITE__CMD, 0x70050000, 0x0000000000000000 // 130
, RDSPIN_CMD, 0x70050000, 0x0000000000000004, 0xffffffffffffffff, 0x00000064 // 131
<...>
, RDnCMP_CMD, 0x70060020, 0x7c9280d37ccc8118 // 3898
, WRITE__CMD, 0x70060018, 0x000000000000001f // 3899
, RDnCMP_CMD, 0x70060020, 0x7cf0815a7d1181a5 // 3900
};
#define dft_size (sizeof(dft_playback)/sizeof(uint64_t))
#define dft_totalCommands 3900
#endif

## Slide 7: LLKI Supports??
TileLink CrossBar
RISC-V
TLMaster
Core TileLik Wrapper (Chisel)
Logic Locked Core
(Verilog or Netlist)
Core RegisterSet
Interface
(Chisel)
LLKI-PP
LLKI-Discrete
Core Specific
Discrete IOs
Core TileLik Wrapper (Chisel)
Logic Locked Core
(Verilog or Netlist)
Core RegisterSet
Interface
(Chisel)
LLKI-PP
LLKI-Discrete
Core Specific
Discrete IOs
Core TileLink Wrapper (Chisel)
Logic Locked Core
(Verilog or Netlist)
Core RegisterSet
Interface
(Chisel)
LLKI-Reg
LLKI-Discrete
Core Specific
Discrete IOs
SRoT
TLSlave
TLMaster
Logic unlocking path
Logic path

## Slide 8: Unit Testbench with LLKI Supports
Modified TL wrapper extracted from VCShell.v (to add LLKI’s)
LLKI-PP (Chisel)
Core register Interface Set
Core with LLKI_IF
Core
(RTL)
Core
LLKI-Discrete
IF
LLKI-Discrete
Bus
Core specific
Bus
LLKI-PP
BFM
LLKI-Discrete
BFM
LLKI-TL
BFM
SRoT
BFM
Cycle-by-cycle
Playback
<core>_stimulus.txt
<core>_playback.h
TLplayback.sv
TL-bus
TL-core peripheral bus
Purple blocks: used in cycle-accurate testbench
Green blocks: used in transaction-accurate testbench
BFM Blocks
HW
Blocks